## Slide 1
-
Control System Design – T5 Robotics
Control of the ball in the tube
Team:
Ankit Pandey
Tigran Pletser
Emmanouil Stivaktakis
Julien Van Delft

## Slide 2: Plant description
Components:
DC current driven motor
Fan attached to the motor
Tachometer to measure velocity
  Linear between -1400 rpm and 3600 rpm
Infrared sensor to measure the ball position
  Two linear zones, 0 to 60cm and 60 to 180cm

## Slide 3: Requirements
Basic requirement
Stabilisation of the ball at a fixed position without any steady state error
More advanced requirements
Switch between two different points with a maximum of 1 cm overshoot
Switch between two different points with a maximum of 1 cm overshoot in maximum 2 seconds.

## Slide 4: Methodology
Current-Motor system :
current as input and fan velocity as output
Fan-Ball system
fan velocity as input and ball position as output
Using cascade control method, we transform a system with 1 input/2 ouputs into 2 SISO systems. And by using the Gray box method (with the equations on the next slide), we find those 2 subsystems :
Inner loop and outer loop will be identified, validated with the real plant and controlled

## Slide 5: Physical relationships
Current-motor system
The current-motor system has the form of a simple first order system
Fan-ball system
The fan-ball system reduces to an integrator and a first order system
But the pole has low impact on the system so the second system can be approximated by an integrator with a gain

## Slide 6: Inner loop - Identification
Response to a small step
No dead zone
Response to a huge positive step
Upper saturation to 9.6V or 3840 rpm
Response to a huge negative step
Lower saturation to –10V or -4000rpm

## Slide 7: Inner loop - Identification
Identified transfer function
Current into Fan velocity
Validation

## Slide 8: Inner loop - Regulation
Main characteristic :
Reacts fast to the input
Static error can be neglected
=> Proportionnal regulation
With Pade' approximant and a sampling time of 0.01, we find this root locus
We find a max Kp without overshoot of 12.4
By plotting the Bode diagram of the sub-system (including real ZOH)
We find a maximal gain of 12300

## Slide 9: Inner loop - Regulation
By testing, we find that the equilibrium point of the ball is 6,2V which leads to around 6,4V input as the static error is non-zero
The maximum gain while avoiding the motor saturation (10V) is then Kp = 2.777
We used a gain of 2,775 which gives us a settling time of about 0,25s
We then use our regulation on the real plant and find that it matches with our model

## Slide 10: Outer loop – infrared sensor modelisation
2 different linear zones
Between 0m and 1.2m (in the tube) or 1.2V and 2.5V
  with a slope of 1.083
Between 1.2m and 1.8m or 2.5V and 7.3V
  with a slope of 8.03

## Slide 11: Outer loop - Identification
We want study the variation of the ball around the equilibrium
The equilibrium point is 6.2V at the input of the second system
Introducing a step of 0.85m (1V) above the equilibrium value

## Slide 12: Outer loop - Identification
Saturation at the output are 0m (bottom) and 1.8m (top)
1.2V is the offset value given to 0m
0.174 is an experimental value to cancel the negative offset when the fan is rising to the equilibrium speed

## Slide 13: Outer loop - validation
Comparison of the outer loop model with the real plant outer loop both in open loop and closed loop
Closed loop with a Kp of 1 for testing
Excellent match between the model and the plant

## Slide 14: Introduction of noise in the model
In the real plant, both sensors are producing noise
Noise is added in the model to simulate more accurately the plant

## Slide 15: Outer loop – P regulation
The second system is already an integrator ==> A P-regulator is enough to acheive basic requirement
Rltool is used on the outerloop to find a P-regulator that could maybe satisfy advanced requirements in the upper zone
Settling time of 2s
1cm/(180cm-120cm) = 1.666% overshoot (upper zone)
Kp = 0.9821 is a good compromise between a low settling time and no overshoot

## Slide 16: Outer loop – P regulation
Test of the regulation on the model
Test of the regulation on the plant
It fulfills the requirements for the model but not for the real plant probably due to the simplification we made on the form of the second model

## Slide 17: Outer loop – PD regulation
To decrease the settling time and the overshoot, derivative regulation is added
Rltool with the same requirements for the upper zone
The zero is placed on the pole in order to have a pole-zero cancellation decreasing the settling time
The minimum Kp is 0.70753 and the N is set to 5

## Slide 18: Outer loop – PD regulation
Checking the phase and gain margin of this PD regulator with the ZOH
Gain and phase margin are above the usual values of 6dB and 30 degrees
Test of the PD regulator on the model
Test of the PD regulator on the plant
The plant and the model both respects all requirements but in the plant lots of noise appears at 1.3m which is probably due to the limit of the sensor linear zones

## Slide 19: Extension to full tube
To take into account the change of slope in the 0-120 cm zone, another regulation was designed using an overshoot percentage of 0,833% and the sensor gain of 1.083
We thus found have 2 different regulations to control the full tube
Which gave us a gain of 5.0766 and this regulation on the plant

## Slide 20: Implementation
Discrete-time regulation needs to be implemented
Matlab function is used with a sampling time of 0.01s
The previous derivative regulator is transformed in its z-form using c2d
As we know that

## Slide 21: Implementation
The value of Kp is adapted depending on the ball position at the beginning of the code
The next input is computed by
At which the equilibrium value is added
Comparison of CT and DT PD regulation
The error is the difference between the real position and the reference

## Slide 22: Discussion
Further improvement would be a third regulator or a filter to respect the requirements in the 130-150cm zone in which noise appears
Our interpretation of this noise is that it comes from the non linearity of the sensor in that zone

## Slide 23
Q&A

## Slide 25: Codes

## Slide 26: Codes